## Slide 1: Lab 4
I/O in an Embedded System
Julio César Almada Fuerte
A00226046
ITE

## Slide 2: PART 1
Use the 7-segment display to display a digital number, but now you are going to use the key buttons.
KEY0: Sets the number on the display to 0.
KEY1:Increments displayed number.
KEY2:Decrements displayed number.
KEY3:Blanks the display, it is turned on until any other key is pressed

## Slide 3
Push buttons are detected through polling, to read the Data register. There you can see when a button is pressed.
If not pressed, data register provides 0
If “i” button is pressed, data register provides the value 1 in “i” position.

## Slide 5: PART 2
Counter from 0 to 99 in a loop, increments every .25 seconds. (Delay provided)
Counter should stop if a button is pressed. (Use the Edgecapture register, when a button press happens, it is set to 1 and remains until anything is written into the register).

## Slide 7: PART 3
Does the same of part 2, but now using the A9 Private timer registers for the delays.
Write a value to the Load register, set E to 1 to start the timer. The counter will reload the Load register and continue if A is 1. When it reaches 0, F is set to 1(This bit has to be polled).To reset F write 1 into it.

## Slide 9: PART 4
Use all your knowledge acquired to implement a real-time clock. Display it on the 7 – segments. It has to work on this format= SS:DD (Seconds:Hundredths of a second).
Polled I/O with the A9 Private timer.
Should stop/run with any button press.